## Slide 1
Reconfigurable Computing 2
Using Kernels and Unified Shared Memory
Greg Stitt
Associate Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Framework for SYCL/DPC++
Single Source
  Both host code and device code exist in the same file
Application Code
  Setting up devices
  Managing queues for different tasks
  Allocating data for devices
Kernel Code
  Any code that runs on the target devices
  Typically expressed as a lambda function
  Certain restrictions
    Dynamic memory allocation
    Static variables
    Function pointers
    Etc.

## Slide 3: Writing Code for Kernels
C++ Lambda Functions
  Very common practice for parallel programming
  Used to create anonymous, inline functions
  [capture-list] (params) -> return {body}
    Capture list is the set of variables to be returned
    Params is set of variables being passed in
    Return is the return type
    Body is the function code
    Capture list and params can be by value or reference
SYCL Restrictions
  Capture list and params must be by value only
  Return type must be void

## Slide 4: Different Types of Kernels
Single Task
  Executes a single instance of a function on device
Parallel For
  Executes multiple instances based on a range parameter
  Should not be thought of as a “for loop”
  Multiple instances are run at the same time

## Slide 5: Parallel For
Parallel for is the most common type of Kernel
Best at exploiting “embarrassing data parallelism”
  Embarrassing parallelism requires little effort to separate tasks
  Common when tasks have little to no dependency
  Ex: Manipulating pixels in an image, matrix multiplication
Must specify ranges when calling parallel for

## Slide 6: Pipelining on FPGA via SYCL
Spatial pipeline
  We can fill a pipeline with different tasks of a kernel
  Consider effects on clock frequency
  Routing issues as placement increases

## Slide 7: Kernels on FPGAs
Multiple kernels can run on FPGA
Kernels can run concurrently
Each kernel occupies its own space

## Slide 8: Unified Shared Memory
How to manage data between host and device?
Device needs to data to run
Host needs to get data back from device
3 types of memory:
  Device allocations: kernels can read and write but host cannot
  Host allocations: host memory that can accessed remotely by device via bus like PCI-express
  Shared allocations: memory that can migrate from host to device freely automatically
    Device no longer must use bus system to write data

## Slide 9: Managing Memory with USM
USM is a pointer-based strategy
Memory is dynamically allocated via malloc or new
Different functions to differentiate between host or device
Returns pointers to memory
Memory must be freed when program ends

## Slide 10: Memory Movement with USM
Explicit memory movement between host and device
  Utilize memcpy to specify source and destination
Memory movement can also be implicit
  Memory allocation must be specified as shared
  Compiler will handle copies and movement as needed
  Safer but not as optimized as explicit contrl

## Slide 11: Using Buffers
Buffers can be used as an alternative to USM
High-level abstraction for data
  Data is not tied to single memory location
  Both host and device can access the buffer
Data from a buffer cannot be directly managed
  Must make use of accessor object
  Accessor objects can be read only, write only, or both
  Accessor objects must be created in reference to a particular buffer

## Slide 12: Buffer and Accessor Example