## Slide 1: Programming SYCL for FPGA

## Slide 2: SYCL for FPGAs
FPGA support is not natively built into SYCL, but instead relies on vendor supported options
DPC++ supports FPGA selectors and dataflow pipes
Optimal FPGA performance will require you to reference the vendor’s documentation

## Slide 3: When to use an FPGA
A CPU/GPU will reuse the same part of the chip multiple times to complete a set of instructions
By contrast, an FPGA benefits from its reconfigurable nature and can layout the entire instruction set on hardware at once
To achieve maximum efficiency in this spatial architecture, FPGAs exploit pipeline parallelism
For an optimal pipeline, a new output is produced each cycle (after the initial time to generate the first output)
In DPC++, pipeline architecture is performed automatically by the compiler

## Slide 4: When to use an FPGA
FPGAs excel at performing bitwise calculations with custom bit lengths, where adders/multipliers in an ASIC will have constant data widths
By their nature, FPGAs have registers to hold internal values, which means they don’t need to communicate with memory
This makes them good candidates for algorithms that need to pass data between different sections with strict timing dependencies

## Slide 5: Developing for FPGA
Initial code
Perform functional validation using an FPGA emulator
  Compile time: seconds
Generate static reports for timing and spatial analysis
  Compile time: minutes
Perform full hardware compile and generate bitstreams
  Compile time: hours

## Slide 6: Developing for FPGA
Due to their long compile times, we must generate the FPGA binaries in advance (ahead-of-time compilation) and embed them in the DPC++ executable
  DPC++ uses a version of Quartus to perform place-and-route optimizations
At runtime, we choose an accelerator for the code (fpga_selector), and the DPC++ runtime will automatically program the FPGA

## Slide 7: Pipeline Efficiency
For maximum utilization, the pipeline must be kept busy with data
ND-Range
  Useful when work-items require little to no communication
Loops
  Handles data dependencies by partially overlapping iterations of the loop

## Slide 8: Pipes
In DPC++, pipes are FIFO implementations used to create modular code to be run on an FPGA
Pipes store information in registers on the FPGA, which allows for communication between kernels without using off-chip memory
Types of pipes include Inter-kernel, Intra-kernel, Host, and I/O