## Slide 1
Reconfigurable Computing 2
Using SYCL and DPC++ for FPGAs
Greg Stitt
Associate Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: SYCL and FPGAs
FPGA support is not natively built into SYCL, but instead relies on vendor supported options
  Different compilers (DPC++, triSYCL, ComputeCPP) will have different options
Optimal FPGA performance will require you to reference the vendor’s documentation
  For DPC++, Intel provides references in the oneAPI documentation
DPC++ supports dataflow pipes, FPGA emulators, FPGA selectors, and additional tools for timing/spatial analysis
  These features are available via Intel extensions provided in the oneAPI toolkit

## Slide 3: When to use an FPGA
FPGAs can layout the entire instruction set on hardware at once
  CPUs and GPUs will reuse the same part of the chip multiple times to complete a set of instructions
FPGAs excel at performing bitwise calculations with custom bit lengths
  Adders and multipliers in an ASIC will have constant data widths
FPGAs have registers to hold internal values, which means they don’t need to communicate with memory
  This makes them good candidates for algorithms that need to pass data between different sections with strict timing dependencies
FPGAs exploit pipeline parallelism to achieve maximum efficiency
  In DPC++, pipeline architecture is performed automatically by the compiler

## Slide 4: Developing for FPGAs
Typical development cycle:
  Write/edit code
  Perform functional validation using an FPGA emulator
    Compile time: seconds
  Generate static reports for timing and spatial analysis
    Compile time: minutes
  Perform full hardware compile and generate bitstreams
    Compile time: hours

## Slide 5: Developing for FPGAs
Due to their long compile times, FPGA binaries are generated in advance and embedded in the DPC++ executable
  Full compilation with DPC++ requires Quartus Pro to perform place-and-route
  Recompile time can be shortened by keeping host code and FPGA code in separate files
    Inform the DPCPP compiler to perform an accelerated recompile
The FPGA emulator extension can test basic functionally without Quartus
  The emulator does NOT provide an accurate representation of timing and undefined behavior
At runtime, we choose a device and the DPC++ runtime will automatically program/emulate the FPGA
  Default FPGA/emulator selectors are provided in the oneAPI toolkit with Intel FPGA extensions
    Custom selectors can be programmed to select a device based on a set of criteria

## Slide 6: Developing for FPGAs
Pipes:
  Pipes are an Intel-supported SYCL extension that adds FIFO implementations to support spatial architectures on FPGAs
    Extension is included with the oneAPI base toolkit
  Pipes store information in registers on the FPGA, which allows for communication between kernels without using off-chip memory
    Types of pipes:
      Inter-kernel, Intra-kernel, Host, and I/O
  SYCL compliant pipes are defined as a class with static members
    Pipes are declared using a type alias
    Identifier for the pipe, data type, capacity must be specified

## Slide 7
Pipeline Efficiency
For maximum utilization, the pipeline must be kept busy with data
ND-Range
  Useful when work-items require little to no communication
Loops
  Handles data dependencies by partially overlapping iterations of the loop

## Slide 8
Loop Unrolling
Loop unrolling increases parallelism by duplicating compute logic in a loop
Instead of x iterations, execution occurs in x/y iterations where y is the unroll factor
Full unrolling is when x=y, partial unrolling is when x >y
The tradeoff is throughput vs resource utilization

## Slide 9
Loop-carried Memory Dependencies
Where memory access inside a loop cannot proceed until a read or write from a previous iteration has finished.
  True Dependence (read-after-write)
    read in current iteration must wait for write from previous iteration in the same location
  Anti Dependence (write-after-read)
  Output Dependence (write-after-write)

## Slide 10
Loop-carried Memory Dependencies
Compiler attempts to statically determine dependencies
Some statements assumed dependent
Precise dependence information improves pipeline parallelism generated by compiler

## Slide 11
Loop-carried Memory Dependence Examples
Basic true-dependence
  Each iteration reads from the location written to in the previous iteration
  Pipeline cannot generate new iteration until previous is done.

## Slide 12
Loop-carried Memory Dependence Examples
Statically-unknown indexing expression
  Compiler cannot infer the true access pattern
  Statements assumed dependent for all iterations

## Slide 13
Loop-carried Memory Dependence Examples
Loop-independent dependence
  Dependencies only spanning one iteration of a loop
  Don’t affect compiler’s datapath generation

## Slide 14
Loop-carried dependence distance
Number of iterations between the source and sink of the dependency.
Iteration k may not execute until iteration k-10 has completed, so the distance is 10 iterations.

## Slide 15
ivdep
ivdep informs the compiler that no reads/writes in a loop have dependencies
The generated datapath will issue new iterations every cycle
ivdep(a) states there are no dependencies for the array or pointer a
  Always specify an array or pointer
  Undefined behavior will occur if ivdep is applied when dependencies exist