## Slide 1
Reconfigurable Computing 2
Introduction to SYCL and DPC++
Greg Stitt
Associate Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: Why should you care?
Goal - offload computations to accelerator device
Problem - different devices typically require specific programming languages
Solution - single-source code that can target multiple types of devices

## Slide 3
Why use SYCL?
3
Many different devices are used for workload acceleration
  CPUs
  GPUs
  FPGAs
Writing custom-tailored code for accelerators is not flexible or distributable
  Code cannot be shared or re-used with other devices
  Code may need to be entirely re-written if changing devices
SYCL allows for one higher-level code base to be run on a variety of devices
  The same code can be re-used on different devices
  Code can be more easily tweaked for different applications
Libraries contain pre-written code custom-made for each architecture
  Every high-level function call is optimized for each supported device
  Performance theoretically equivalent to writing lower-level code manually
  Much faster to write than lower-level code, especially RTL

## Slide 4
What is SYCL?
4
SYCL
  An abstraction layer that builds upon OpenCL
    Framework for programming heterogeneous platforms
  Allows for data parallel programming for C++
    Higher level than OpenCL but has seamless integration with OpenCL and C++ libraries
  Targets a variety of hardware accelerators using a unified, high-level programming language
    CPUs
    GPUs
    FPGAs

## Slide 5
What is DPC++?
5
Data Parallel C++
  Extends the SYCL framework
    The programming language used to write SYCL programs
    Open source
    Aims to become a core SYCL extension
  Incorporates SYCL standard for data parallelism and heterogeneous programming
    Very similar to C++ but with extra functionality for data parallelism
  Offloads computation from host computer to accelerator
    Programmer specifies which code to offload to which accelerator in code

## Slide 6: Basic SYCL Program
In any SYCL program, the host must:
  Choose an accelerator device
  Tell the device what to do
  Transfer data between host and device

## Slide 7: Basic SYCL Program
In any SYCL program, the host must:
  Choose an accelerator device
    Device is chosen with the ”device selector” class
    Accelerator support is determined by the compiler
      Intel’s DPC++ compiler supports Intel GPUs via OpenCL
      Intel FPGAs are supported through their SYCL extension
    Default selectors will choose the most capable device at runtime
      gpu_selector, cpu_selector, accelerator_selector, fpga_selector
    Alternatively, we can extend the device selector class for custom selection criteria
  Tell the device what to do
  Transfer data between host and device

## Slide 8: Basic SYCL Program
In any SYCL program, the host must:
  Choose an accelerator device
  Tell the device what to do
    Interface between host and device is defined by the “queue” class
      Each queue is bound to a single device chosen by the device selector
    The host submits tasks to the queue and continues to execute the program
      The host can also monitor the queue for completion, timing, errors, etc.
  Transfer data between host and device

## Slide 9: Basic SYCL Program
In any SYCL program, the host must:
  Choose an accelerator device
  Tell the device what to do
  Transfer data between host and device
    Implicit data management is commonly achieved with “buffer” and “accessor” classes
      Buffers are references to the original data in memory
      Accessors are the only way to read/write data referenced by the buffer
    Explicit data management is achieved only through Unified Shared Memory or USM
      Memory is allocated directly with “malloc_host” or “malloc_device”

## Slide 10: Basic SYCL Program
Host
FPGA
GPU
AI
Host chooses from available
accelerator devices using
‘device_selector’ class

## Slide 11: Basic SYCL Program
Host
GPU
Host establishes layer to give instructions to and receive feedback from the device
Queue
C[i] = A[i] + B[i]

## Slide 12: Basic SYCL Program
Host
Host
GPU
Host establishes layer to give instructions to and receive feedback from the device
GPU
Memory
Queue
Memory

## Slide 13: Basic SYCL Program
Host
GPU
Host transfers data to and from the device
GPU
Mem
Mem
Queue
Buffer
Accessor

## Slide 14
Abstractions used for submitting work to a device
  Bound to a single device upon creation
  Device is selected via device_selector class
  Can allow selector to select from a class of devices or write custom selector
Tasks submitted to queue are offloaded to device when conditions are met
  Host continues execution of the program after submission to the queue
Task execution can be in-order or out-of-order
  Out-of-order by default, execution order determined by runtime
  Can be instantiated with the in-order property for implicit dependency specification
Queues

## Slide 15
    auto q = sycl::queue(sycl::default_selector()); //select default device for queue (CPU usually)
    q.submit([&](sycl::handler &cgh) { auto os = sycl::stream{128, 128, cgh}; //define the queue interface
    cgh.single_task<class hello_world>([=] { os << "Hello World!\n"; }) //submit task to queue
  q.wait(); //wait for all queued tasks to finish
Queues Example

## Slide 16
Data abstractions of a certain C++ type
  Can be scalar data types, vectors, or other user-defined class/structure
    Must not require the use of copy constructors for copying
Represent data objects, not memory addresses
  Cannot be accessed like C++ arrays
  Accessors must be used to read from and write to buffers
A single buffer may be distributed across multiple locations
  Between discrete memory locations and devices
An empty buffer may be created by specifying a range for size
  Data must later be initialized before the buffer can be read from
Existing host data may be used to initialize a new buffer
  Accomplished by invoking a constructor that takes a pointer to an existing host allocation
May also be created from existing cl_mem objects if using OpenCL compatibility
Buffers

## Slide 17
// Create a buffer of 2x5 ints using the default allocator
buffer<int, 2, buffer_allocator> b1{range<2>{2, 5}};
// Create a buffer of 2x5 ints using the default allocator and CTAD for range
buffer<int, 2> b2{range{2, 5}};
// Create a buffer of 20 floats using a default-constructed std::allocator
buffer<float, 1, std::allocator<float>> b3{range{20}};
// Create a buffer of 20 floats using a passed-in allocator
std::allocator<float> myFloatAlloc;
buffer<float, 1, std::allocator<float>> b4{range(20), myFloatAlloc};
Buffers Examples

## Slide 18
The only way in which to read from or write to buffers
Can be instantiated with read, write, or read_write access modes
  Accessors are read_write by default
Using appropriate access modes is important
  Provides implicit information used to help the runtime manage memory
    For example: read mode tells the runtime that it does not need to copy memory back to the host, as the device has not changed it.
  Appropriate use of access modes will help the runtime optimize kernel scheduling and data migration
Accessors

## Slide 19
Objects that specify a task and its dependencies
Typically in the form of C++ Lambda functions
  The only parameter is a reference to a handler object
Passed as an argument to a queue object’s submit() function
Command Group structure:
  Exactly one action (and no more)
    Either device code submitted for execution or manual memory operations such as copy
  Host code that defines dependencies
    Restricts when asynchronous execution of the submitted work can begin. For example: creation of accessors or buffers
Command Groups

## Slide 20
Q.submit([&](handler& h) { // function called on host
accessor acc{ B, h }; // host code defining accessor, setting up dependencies
h.parallel_for(size, [=](auto& idx) {
acc[idx] = idx; // Device code to be run when runtime dependencies are met
});
});
Source: Data Parallel C++, James Reinders et al. pg. 27
Device Work Submission Example

## Slide 21
vector_addition.cpp
  https://github.com/BenjaminMFindley/Reconfig-2-SYCL-DPCPP/blob/main/Examples/vector_addition/vector_addition.cpp
Example

## Slide 22
Running heterogeneous computing systems efficiently requires careful handling of data
  Data must be available for accelerator execution as promptly as possible as any idle time is wasted
There are two methods for managing data in DPC++
  Unified Shared Memory (USM)
  Buffers
Device code requires data as input and may output its own data
Devices may have their own distinct memory which cannot be accessed by the host
  Proper data management deals with the safe and efficient storage and movement of data between memory pools
Remote Accesses are accesses to data in another device’s memory
  Very slow
Local Accesses are accesses to data in directly-attached memory
  Much faster than remote accesses
  It is desirable for a device to utilize local memory for computation
    May require manual movement of data between memory pools to ensure data is in local scope
Data Management

## Slide 23
Dependencies between tasks may be implicit or explicit
Explicit dependency refers to dependency between computations
  Most relevant to code utilizing USM for data management
  Dependencies specified using events
Implicit dependency refers to dependency between data accesses
  Relevant to code utilizing buffers for data management
  Dependencies specified through accessors
Dependency

## Slide 24
Memory Management can be either implicit or explicit
  Explicitly copied within the program itself
  Implicitly copied by the runtime
Implicit Memory Management
  Handled automatically by the runtime
  Simple and safe
  Often at the cost of potential performance
Explicit Memory Management
  Defined manually by the programmer
  May be optimized for better performance
    For example: transfer data while device is busy with execution
  Time consuming and error prone
  Should be reserved for the most performance-critical areas
Implicit vs Explicit Memory Management

## Slide 25
Different tasks may depend on one another’s data
Data dependency exists in one of three forms
  Read-after-write: Task B must wait for Task A to read before it can write
  Write-after-read: Task B must wait for Task A to write before it can read
  Write-after-write: Task B must wait for Task A to write before it can write
These relationships are specified implicitly via
  Accessor access modes
  Task ordering
    If two accessors exist for the same data, whichever task is submitted first will be executed first
    An implicit dependency is created based on the types of access
Data Dependency (Implicit)

## Slide 26
vector_addition_with_dependency.cpp
  https://github.com/BenjaminMFindley/Reconfig-2-SYCL-DPCPP/blob/main/Examples/vector_addition/vector_addition_with_dependency.cpp
Example

## Slide 27
A queue’s submit() function returns an event
Event objects can be captured and referenced for other purposes
  wait()
  depends_on()
depends_on() is a handler function used to specify dependency
  Specifies events on which the current operation depends
  Takes an event or vector of events as parameters
  Will wait until all specified events have finished before continuing execution
Computational Dependency (Explicit)

## Slide 28
Pointer-based memory management system, similar to C/C++ malloc() or new
Defines a unified virtual memory space shared between host and devices
  A pointer is valid both on the host and any devices, so no translation is necessary
Defines three types of allocation
  Device
    Explicit, accomplished via memcpy() function as part of the queue and handler classes
    Located on device-attached memory
    Only accessible via device. Data must be copied explicitly to move between host and device
  Host
    Implicit
    Accessible via both host and device
    Data accessed on host memory by devices does not transfer into local device memory
      Sent via bus such as PCI-E
  Shared
    Implicit
    Accessible via both host and device
    Can migrate between host and device, allowing for faster execution on device. Occurs automatically via runtime
  All allocations are performed by the host
Universal Shared Memory (USM)

## Slide 29
vector_addition_usm.cpp
  https://github.com/BenjaminMFindley/Reconfig-2-SYCL-DPCPP/blob/main/Examples/vector_addition/vector_addition_usm.cpp
Example

## Slide 30
Default selector chooses most capable device at runtime
Device selector classes exist to choose from specific class of device
  gpu_selector
  cpu_selector
  accelerator_selector
  fpga_selector exists via intel extension
  Useful for quick development, but typically want specific device for a task
Custom selectors created by extending device_selector base class
virtual int operator()(const device &dev) const {
/* Device selection logic */
}
Device Selection

## Slide 31
operator() is key to device selection
  Runs on each available device
  Returns an integer score for each device
    Device which returns highest score is selected
    Devices which return negative scores will never be selected
User is free to define any logic for scoring
  Allows for arbitrarily complex device selection logic
  In simple cases, selecting based on device name or vendor is sufficient
Custom Device Selection

## Slide 32
class my_selector : public device_selector {
public:
int operator()(const device &dev) const override {
if (
dev.get_info<info::device::name>().find("Arria") != std::string::npos &&
dev.get_info<info::device::vendor>().find("Intel") != std::string::npos) {
return 1;
}
return -1;
}
};
Source: Data Parallel C++, James Reinders et al. pg. 46
Custom Device Selection Example

## Slide 33
vector_addition_with_timing.cpp
  https://github.com/BenjaminMFindley/Reconfig-2-SYCL-DPCPP/blob/main/Examples/vector_addition/vector_addition_with_timing.cpp
Example