## Slide 1
Programming SYCL for FPGA

## Slide 2
SYCL for FPGAs
FPGA support is not natively built into SYCL, but instead relies on vendor supported options
DPC++ supports FPGA selectors and dataflow pipes
Optimal FPGA performance will require you to reference the vendor’s documentation

## Slide 3
When to use an FPGA
A CPU/GPU will reuse the same part of the chip multiple times to complete a set of instructions
By contrast, an FPGA benefits from its reconfigurable nature and can layout the entire instruction set on hardware at once
To achieve maximum efficiency in this spatial architecture, FPGAs exploit pipeline parallelism
For an optimal pipeline, a new output is produced each cycle (after the initial time to generate the first output)
In DPC++, pipeline architecture is performed automatically by the compiler

## Slide 4
When to use an FPGA
FPGAs excel at performing bitwise calculations with custom bit lengths, where adders/multipliers in an ASIC will have constant data widths
By their nature, FPGAs have registers to hold internal values, which means they don’t need to communicate with memory
This makes them good candidates for algorithms that need to pass data between different sections with strict timing dependencies

## Slide 5
Developing for FPGA
Initial code
Perform functional validation using an FPGA emulator
  Compile time: seconds
Generate static reports for timing and spatial analysis
  Compile time: minutes
Perform full hardware compile and generate bitstreams
  Compile time: hours

## Slide 6
Developing for FPGA
Due to their long compile times, we must generate the FPGA binaries in advance (ahead-of-time compilation) and embed them in the DPC++ executable
  DPC++ uses a version of Quartus to perform place-and-route optimizations
At runtime, we choose an accelerator for the code (fpga_selector), and the DPC++ runtime will automatically program the FPGA

## Slide 7
Pipeline Efficiency
For maximum utilization, the pipeline must be kept busy with data
ND-Range
  Useful when work-items require little to no communication
Loops
  Handles data dependencies by partially overlapping iterations of the loop

## Slide 8
Pipes
In DPC++, pipes are FIFO implementations used to create modular code to be run on an FPGA
Pipes store information in registers on the FPGA, which allows for communication between kernels without using off-chip memory
Types of pipes include Inter-kernel, Intra-kernel, Host, and I/O
SYCL compliant pipes are defined as a class with static members.

## Slide 9
Pipes
Pipes are declared using a type alias
Identifier for the pipe, data type, capacity must be specified.

## Slide 10
Loop Unrolling
Loop unrolling increases parallelism by duplicating compute logic in a loop
Instead of x iterations, execution occurs in x/y iterations where y is the unroll factor
Full unrolling is when x=y, partial unrolling is when x >y
The tradeoff is throughput vs resource utilization

## Slide 11
Loop-carried Memory Dependencies
Where memory access inside a loop cannot proceed until a read or write from a previous iteration has finished.
  True Dependence (read-after-write)
    read in current iteration must wait for write from previous iteration in the same location
  Anti Dependence (write-after-read)
  Output Dependence (write-after-write)

## Slide 12
Loop-carried Memory Dependencies
Compiler attempts to statically determine dependencies
Some statements assumed dependent
Precise dependence information improves pipeline parallelism generated by compiler

## Slide 13
Loop-carried Memory Dependence Examples
Basic true-dependence
  Each iteration reads from the location written to in the previous iteration
  Pipeline cannot generate new iteration until previous is done.

## Slide 14
Loop-carried Memory Dependence Examples
Statically-unknown indexing expression
  Compiler cannot infer the true access pattern
  Statements assumed dependent for all iterations

## Slide 15
Loop-carried Memory Dependence Examples
Loop-independent dependence
  Dependencies only spanning one iteration of a loop
  Don’t affect compiler’s datapath generation

## Slide 16
Loop-carried dependence distance
Number of iterations between the source and sink of the dependency.
Iteration k may not execute until iteration k-10 has completed, so the distance is 10 iterations.

## Slide 17
ivdep
ivdep informs the compiler that no reads/writes in a loop have dependencies
The generated datapath will issue new iterations every cycle
ivdep(a) states there are no dependencies for the array or pointer a
  Always specify an array or pointer
  Undefined behavior will occur if ivdep is applied when dependencies exist