## Slide 1
Pipeline Efficiency
For maximum utilization, the pipeline must be kept busy with data
ND-Range
  Useful when work-items require little to no communication
Loops
  Handles data dependencies by partially overlapping iterations of the loop

## Slide 2
Loop Unrolling
Loop unrolling increases parallelism by duplicating compute logic in a loop
Instead of x iterations, execution occurs in x/y iterations where y is the unroll factor
Full unrolling is when x=y, partial unrolling is when x >y
The tradeoff is throughput vs resource utilization

## Slide 3
Loop-carried Memory Dependencies
Where memory access inside a loop cannot proceed until a read or write from a previous iteration has finished.
  True Dependence (read-after-write)
    read in current iteration must wait for write from previous iteration in the same location
  Anti Dependence (write-after-read)
  Output Dependence (write-after-write)

## Slide 4
Loop-carried Memory Dependencies
Compiler attempts to statically determine dependencies
Some statements assumed dependent
Precise dependence information improves pipeline parallelism generated by compiler

## Slide 5
Loop-carried Memory Dependence Examples
Basic true-dependence
  Each iteration reads from the location written to in the previous iteration
  Pipeline cannot generate new iteration until previous is done.

## Slide 6
Loop-carried Memory Dependence Examples
Statically-unknown indexing expression
  Compiler cannot infer the true access pattern
  Statements assumed dependent for all iterations

## Slide 7
Loop-carried Memory Dependence Examples
Loop-independent dependence
  Dependencies only spanning one iteration of a loop
  Don’t affect compiler’s datapath generation

## Slide 8
Loop-carried dependence distance
Number of iterations between the source and sink of the dependency.
Iteration k may not execute until iteration k-10 has completed, so the distance is 10 iterations.

## Slide 9
ivdep
ivdep informs the compiler that no reads/writes in a loop have dependencies
The generated datapath will issue new iterations every cycle
ivdep(a) states there are no dependencies for the array or pointer a
  Always specify an array or pointer
  Undefined behavior will occur if ivdep is applied when dependencies exist