## Slide 1
Reconfigurable Computing 2
Using SYCL and DPC++ for FPGAs
Greg Stitt
Associate Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: SYCL and FPGAs
FPGA support is not natively built into SYCL, but instead relies on vendor supported options
  Different compilers (DPC++, triSYCL, ComputeCPP) will have different options
Optimal FPGA performance will require you to reference the vendor’s documentation
  For DPC++, Intel provides references in the oneAPI documentation
DPC++ supports dataflow pipes, FPGA emulators, FPGA selectors, and additional tools for timing/spatial analysis
  These features are available via Intel extensions provided in the oneAPI toolkit

## Slide 3: When to use an FPGA
FPGAs can layout the entire instruction set on hardware at once
  CPUs and GPUs will reuse the same part of the chip multiple times to complete a set of instructions
FPGAs excel at performing bitwise calculations with custom bit lengths
  Adders and multipliers in an ASIC will have constant data widths
FPGAs have registers to hold internal values, which means they don’t need to communicate with memory
  This makes them good candidates for algorithms that need to pass data between different sections with strict timing dependencies
FPGAs exploit pipeline parallelism to achieve maximum efficiency
  In DPC++, pipeline architecture is performed automatically by the compiler

## Slide 4: Developing for FPGAs
Typical development cycle:
  Write/edit code
  Perform functional validation using an FPGA emulator
    Compile time: seconds
  Generate static reports for timing and spatial analysis
    Compile time: minutes
  Perform full hardware compile and generate bitstreams
    Compile time: hours

## Slide 5: Developing for FPGAs
Due to their long compile times, FPGA binaries are generated in advance and embedded in the DPC++ executable
  Full compilation with DPC++ requires Quartus Pro to perform place-and-route
  Recompile time can be shortened by keeping host code and FPGA code in separate files
    Inform the DPCPP compiler to perform an accelerated recompile
The FPGA emulator extension can test basic functionally without Quartus
  The emulator does NOT provide an accurate representation of timing and undefined behavior
At runtime, we choose a device and the DPC++ runtime will automatically program/emulate the FPGA
  Default FPGA/emulator selectors are provided in the oneAPI toolkit with Intel FPGA extensions
    Custom selectors can be programmed to select a device based on a set of criteria

## Slide 6: Developing for FPGAs
Pipes:
  Pipes are an Intel-supported SYCL extension that adds FIFO implementations to support spatial architectures on FPGAs
    Extension is included with the oneAPI base toolkit
  Pipes store information in registers on the FPGA, which allows for communication between kernels without using off-chip memory
    Types of pipes:
      Inter-kernel, Intra-kernel, Host, and I/O
  SYCL compliant pipes are defined as a class with static members
    Pipes are declared using a type alias
    Identifier for the pipe, data type, capacity must be specified

## Slide 7: .cpp to .exe - Compiling
Host executable
FPGA bitstream
SYCL.exe
FPGA bitstream
Verilog RTL code
SYCL.cpp
Host code
Device code
Intel® Quartus® Prime Pro Edition
Intel® oneAPI
DPC++/C++ Compiler
(with FPGA extensions & BSPs)
What happens when you hit compile?
Place and route...
(process takes hours)

## Slide 8: .cpp to .exe - Executing
Data
Data
Data
FPGA bitstream
Host executable
FPGA bitstream
SYCL.exe
Host / CPU
FPGA
PCI-e
FPGA is
programmed…
(data transfer is typical bottleneck)

## Slide 9: FPGA notes
Unlike GPUs, which can use OpenCL APIs at runtime, FPGAs require ahead of time compilation to program the device
This process is vendor specific (it is typically up to the vendor to create a board support package for their devices)
The BSP provides the level of abstraction needed to communicate between the SYCL code and the FPGA
For FPGA, the board support package provided in the intel oneapi base toolkit will convert the SYCL device code to Verilog RTL code (early FPGA image)
This early image is generated in minutes and can be simulated in ModelSim
The OneAPI FPGA toolkit provides a complete BSP for full compilation
Full compilation additionally requires Quartus Prime Pro to perform place and route
Hours later, a bitstream is ready, which can be used to program the FPGA at runtime
Communication with the FPGA board is typically done via PCIe