## Slide 1
Reconfigurable Computing 2
Introduction to SYCL and DPC++
Greg Stitt
Associate Professor
Department of Electrical and Computer Engineering
University of Florida

## Slide 2: What is SYCL?
SYCL
  An abstraction layer that builds upon OpenCL
    Framework for programming heterogeneous platforms
  Allows for data parallel programming for C++
    Higher level than OpenCL but has seamless integration with OpenCL and C++ libraries
  Targets a variety of hardware accelerators using a unified, high-level programming language
    CPUs
    GPUs
    FPGAs

## Slide 3: What is DPC++?
Data Parallel C++
  Extends the SYCL framework
    The programming language used to write SYCL programs
    Open source
    Aims to become a core SYCL extension
  Incorporates SYCL standard for data parallelism and heterogeneous programming
    Very similar to C++ but with extra functionality for data parallelism
  Offloads computation from host computer to accelerator
    Programmer specifies which code to offload to which accelerator in code

## Slide 4: Why use SYCL?
Many different devices are used for workload acceleration
  CPUs
  GPUs
  FPGAs
Writing custom-tailored code for accelerators is not flexible or distributable
  Code cannot be shared or re-used for use with other devices
  Code may need to be entirely re-written if changing devices
SYCL allows for one higher-level code base to be run on a variety of devices
  The same code can be re-used on different devices
  Code can be more easily tweaked for different applications
Libraries contain pre-written code custom-made for each architecture
  Every high-level function call is optimized for each supported device
  Performance theoretically equivalent to writing lower-level code manually
  Much faster to write than lower-level code, especially RTL

## Slide 5: Queues
Abstractions used for submitting work to a device
  Bound to a single device upon creation
  Device is selected via device_selector class
  Can allow selector to select from a class of devices or write custom selector
Tasks submitted to queue are offloaded to device when conditions are met
  Host continues execution of the program after submission to the queue

## Slide 6: Device Selection
Default selector chooses most capable device at runtime
Device selector classes exist to choose from specific class of device
  gpu_selector
  cpu_selector
  accelerator_selector
  fpga_selector exists via intel extension
  Useful for quick development, but typically want specific device for a task
Custom selectors created by extending device_selector base class
    virtual int operator()(const device &dev) const {
    /* Device selection logic */
    }

## Slide 7: Custom Device Selection
operator() is key to device selection
  Runs on each available device
  Returns an integer score for each device
    Device which returns highest score is selected
    Devices which return negative scores will never be selected
User is free to define any logic for scoring
  Allows for arbitrarily complex device selection logic
  In simple cases, selecting based on device name or vendor is sufficient

## Slide 8: Custom Device Selection Example
class my_selector : public device_selector {
public:
int operator()(const device &dev) const override {
if (
dev.get_info<info::device::name>().find("Arria") != std::string::npos &&
dev.get_info<info::device::vendor>().find("Intel") != std::string::npos) {
return 1;
}
return -1;
}
};
Source: Data Parallel C++, James Reinders et al. pg. 46

## Slide 9: Command Groups
Objects that specify a task and its depdendencies
Typically in the form of C++ Lambda functions
  The only parameter is a reference to a handler object
Passed as an argument to a queue object’s submit() function
Command Group structure:
  Exactly one action (and no more)
    Either device code submitted for execution or manual memory operations such as copy
  Host code that defines dependencies
    Restricts when asynchronous execution of the submitted work can begin. For example: creation of accessors or buffers

## Slide 10: Device Work Submission Example
Q.submit([&](handler& h) { // function called on host
accessor acc{ B, h }; // host code defining accessor, setting up dependencies
h.parallel_for(size, [=](auto& idx) {
acc[idx] = idx; // Device code to be run when runtime dependencies are met
});
});
Source: Data Parallel C++, James Reinders et al. pg. 27

## Slide 11: Data Management
Running heterogeneous computing systems efficiently requires careful handling of data
  Data must be available for accelerator execution as promptly as possible as any idle time is wasted
There are two methods for managing data in DPC++
  Unified Shared Memory (USM)
  Buffers
Device code requires data as input and may output its own data
Devices may have their own distinct memory which cannot be accessed by the host
  Proper data management deals with the safe and efficient storage and movement of data between memory pools
Remote Accesses are accesses to data in another device’s memory
  Very slow
Local Accesses are accesses to data in directly-attached memory
  Much faster than remote accesses
  It is desirable for a device to utilize local memory for computation
    May require manual movement of data between memory pools to ensure data is in local scope

## Slide 12: Implicit vs Explicit Memory Management
Memory Management can be either implicit or explicit
  Explicitly copied within the program itself
  Implicitly copied by the runtime
Implicit Memory Management
  Handled automatically by the runtime
  Simple and safe
  Often at the cost of potential performance
Explicit Memory Management
  Defined manually by the programmer
  May be optimized for better performance
    For example: transfer data while device is busy with execution
  Time consuming and error prone
  Should be reserved for the most performance-critical areas

## Slide 13: Universal Shared Memory (USM)
Pointer-based memory management system, similar to C/C++ malloc() or new
Defines a unified virtual memory space shared between host and devices
  A pointer is valid both on the host and any devices, so no translation is necessary
Defines three types of allocation
  Device
    Explicit, accomplished via memcpy() function as part of the queue and handler classes
    Located on device-attached memory
    Only accessible via device. Data must be copied explicitly to move between host and device
  Host
    Implicit
    Accessible via both host and device
    Data accessed on host memory by devices does not transfer into local device memory
      Sent via bus such as PCI-E
  Shared
    Implicit
    Accessible via both host and device
    Can migrate between host and device, allowing for faster execution on device. Occurs automatically via runtime
  All allocations are performed by the host

## Slide 14: Buffers
Data abstractions of a certain C++ type
  Can be scalar data types, vectors, or other user-defined class/structure
    Must not require the use of copy constructors for copying
Represent data objects, not memory addresses
  Cannot be accessed like C++ arrays
  Accessors must be used to read from and write to buffers
A single buffer may be distributed across multiple locations
  Between discrete memory locations and devices
An empty buffer may be created by specifying a range for size
  Data must later be initialized before the buffer can be read from
Existing host data may be used to initialize a new buffer
  Accomplished by invoking a constructor that takes a pointer to an existing host allocation
May also be created from existing cl_mem objects if using OpenCL compatibility

## Slide 15: Accessors
The only way in which to read from or write to buffers
Can be instantiated with read, write, or read_write access modes
  Accessors are read_write by default
Using appropriate access modes is important
  Provides implicit information used to help the runtime manage memory
    For example: read mode tells the runtime that it does not need to copy memory back to the host, as the device has not changed it.
  Appropriate use of access modes will help the runtime optimize kernel scheduling and data migration